## Slide 1: Electronics Simulation
Skills Clinic 2016

## Slide 2: Outline
The need for circuit protection
Types of circuit protection
  Reverse polarity
  Over-voltage
  Over-current
  Complete isolation

## Slide 3: Why is protection needed
Electronics connect to the real word
Non-ideal environment
If not prevent destruction, at least contain it
  Rather destroy a R20 transistor than a R500 processor

## Slide 4: Reverse Polarity protection

## Slide 5: Reverse polarity protection
Simple to accomplish
Almost too simple not to deploy
How
  Place a diode in series with the voltage input

## Slide 6: Over-Voltage protection

## Slide 7: Over-voltage protection
In simple cases
  Zener diode
In more extreme cases
  Crowbar circuits
  Transient Voltage Suppressors (TVS diode) also transorb
Very extreme cases (lightning strike)
  MOVs
  Spark Gaps

## Slide 8: Over-Current Protection

## Slide 9: Over-Current Protection
Glass fuse
  Typical way of doing it
  Non-resettable
  Slow but fast-blow available
Positive / Negative Temperature coefficient devices (PTC, NTC)
  Known as a polyfuse
  Resettable (by removing fault conditions)
  Slow

## Slide 10: Isolation

## Slide 11: When to use isolation
When galvanic isolation is required
When high-power and low-power circuits must be connected
To avoid ground loops from occurring
When various voltage levels are involved
What happens to devices connected here?

## Slide 12: Isolation devices
In AC systems
  Transformers get the job done
In DC systems
  Opto-couplers / Opto-isolators

## Slide 13: Opto-isolators – parameters
Important specifications (consider the 4N25)

## Slide 14: Opto-Isolators - usage

## Slide 15: Opto-couplers - simulation

## Slide 16: Simulation – What is going on here

## Slide 17: Conclusion
Circuit protection is multi-faceted
No hard-and-fast rules
Isolation is very important for “switching” circuits
Simulation of isolation differs slightly from physical circuits

## Slide 18: Next lecture
How to apply circuit protection, and the use of so called “gate drivers”