## Slide 1: Overview of Engineering Design Process
Author: Prof Johann Holm
Date: 2011-10-10

## Slide 2: Overview of the life cycle
Do requirements analysis (ask questions)
Do conceptual design (design system architecture)
Do preliminary design (break into smaller chunks)
  Functional analysis (flow and architecture)
  Requirements allocation (link to functions and resources)
Do detail design (electronics, code, mechanics)
  Design, integrate, test (and test, and test, and test...)
Do manufacturing and / or construction
Use / operate and maintain the system
Phase out / recycle the system
Page 1

## Slide 3: Step 1: Analyse requirements
Start by asking questions about:
What the system must DO (functional capability)
Where the system will be used (to understand transport etc)
Under what conditions (humidity, temperature, shock etc)
How we will use the system (to determine battery life, reliability etc)
How we will manufacture the product (how many, where etc)
How we will test the product (quality assurance)
Refer to B-Specification for a complete set of requirements / questions
Then we determine:
How will we achieve the above – i.e. using what (all the resources)?
Note: The answer to “HOW” is the creative part of the design process
Also: The WHAT-HOW cycle is done iteratively
Page 2

## Slide 4: Notes on WHAT and HOW
High level requirements are addressed by low level resources
That is, WHAT at high level becomes HOW at lower level
Task at high level becomes process at lower level
Example:
using
Do
Operator
Comms and GUI /
Controller and Batt
Alarm panel /
Solar source
WHAT?
HOW?
HOW?
using
Page 3
Monitor alarm / Provide power
Task A
Task B
Task C
System behaviour
Workflow / State diagrams etc
System architecture
Firmware
Module X
Hardware
module Y
Hardware
module Z

## Slide 5: Step 2: Do functional analysis (1)
Do functional flow (“dynamic” – processes at different levels)
Functional flow at operational level:
Then at technical level:
Still at technical level:
The C-code is detail...
What?
How?
What?
How?
What? – How?
becomes...
Page 4
Install unit
Train operator
Operate unit
Detect intrusion
Send intrusion code
Set up IP session
Send IP message
becomes...
becomes...
[ref …]
[ref …]
[ref …]
[ref …]
[ref …]
May also be flowcharts or state diagrams…

## Slide 6: Step 2: Do functional analysis (2)
Do architectural design (“static” – layout at different levels)
NB! Identify and label ALL interfaces and label ALL functional units
Note: The above is at technical level – break down into smaller units for more technical and detail level architectures (i.e. smaller components such as motors, C-code etc)
Page 5
Unit 1.1
Unit 1.2
I/F 1.1
Must be broken down
into smaller units
Will be made up of hardware
and software “units”
Requirements will be “assigned” or
allocated to each functional unit

## Slide 7: Step 3: Allocate requirements
Identify requirements for each task and resource:
  Functional capability (not optional – product MUST do this)
  Performance (“how well” to perform each task – sometimes negotiable)
  Environmental conditions (“design for’s” – actually requirements)
  Usability, testability, maintainability, reliability (design for “ilities”)
NB! You have to define and allocate all requirements
  Ensure requirements are allocated (linked to functions and resources)
Functional capability – does it work?
Performance – how well?
Shock / temperature / humidity / EMC?
Usability?
Testability?
Which one?
using
using
Task
Functional unit
Technology
Page 6
Regulate
PV power
Solar charge
Unit and PSU
Unit 1.2
MIC3230
MIC3231
MIC3232
and UCS1001
Options – select one!
Requirements are “allocated”
to functions, units and interfaces

## Slide 8: How to use “design for’s”
Make a list of all applicable “design for’s”
Compile a list of all specific requirements:
  Usability: Visual feedback (LED’s etc for diagnostics)
  Usability: Simplistic interfaces (what makes things “usable”?)
  Testability: Access to test points, BIT, diagnostics, test jig etc.
  EMC: No large current loops, big ground plane, screening
  EMC: Decoupling caps, etc.
Ensure the lists are complete – make list of 10 of each
Allocate each check list item to ALL applicable elements
Do you see that all “design for’s” are actually just design requirements?
Page 7

## Slide 9: Step 4: “Select” resources
Identify all options
  Do technology research
  Identify selection criteria (cost, space, availability, reliability etc)
  Draw up a decision matrix and make decision as below
Do we buy, or do we make?
  Cost-performance is always an issue
  Availability (single-source / manufacture / time)
  It must “FIT”, i.e. interface requirements MUST be adhered to
 | Cost | Space | Availability | Reliability | Score
Option 1 | 8 | 6 | 8 | 6 | 7
Option 2 | 9 | 8 | 8 | 4 | 6.7
Option 3 | 8 | 8 | 8 | 4 | 6.4
Option 4 | 6 | 4 | 10 | 2 | 5
Weight | 0.3 | 0.1 | 0.2 | 0.4 | 
Page 8
Option 1 – Tech 1
Option 2 – Tech 2
Option 3 – Tech 3
Option 4 – Tech 4

## Slide 10: Step 5: Do detail design
Detail design, integrate, and test are iterative
Ex: Study DC/DC architectures thoroughly (Form)
Identify Technical Performance Measures (How well)
  What makes the DC/DC “good”
  Ex, current capability, max voltage, complexity etc
Identify Design-Dependent Parameters (Using what)
  What influences current, voltage, complexity etc?
  Ex, FET’s RDSON and max voltage / current, layout, etc
Build and test, build and test, build and test...
Integrate with other elements / components (Fit)
Test, test, test... That is, verify and validate
Page 9